## Slide 1
Manual
V BOT
4K HDMI Loop Camera Motorized Head

## Slide 2
White Balance
WB R Gain
(-50 ~ 50)
- When the white balance is set to MANUAL, the indicator lights up in green and the R-GAIN value changes.
WB Manual
Used to set the selected white balance MANUAL using the knob.
WB Auto
Used to set the selected white balance auto.
AWB Hold Off
AWB Hold On
WB B Gain
(-50 ~ 50)
- When the white balance is set to MANUAL, the indicator lights up in green and the B-GAIN value changes.

## Slide 3
Auto Exposure Setting
AE auto
Used to set the selected exposure to AUTO.
AE manual
Used to set the selected exposure to MANUAL using the knob.
AE
Shutter Speed
Up/Down
When auto exposure is set to MANUAL or SHUTTER, the indicator lights up in red and the Shutter speed changes.
AE IRIS Up/Down
When auto exposure is set to MANUAL or IRIS priority, the indicator lights up in red and the Iris value changes
AEGain Up/Down
When auto exposure is set to MANUAL, the indicator lights up in red and the Gain value changes

## Slide 4
Auto Exposure Setting IRIS priority
AE BRight
Up/Down
- When auto exposure is set to
Bright, the indicator lights up
in red and the Bright value
changes.
AE IRIS
Up/Down
- When auto exposure is set to
MANUAL or IRIS priority, the
indicator lights up in
red and the Iris value
AE Gain Limit
Up/Down
- When auto exposure is set
to IRIS priority,
the indicator lights up in red
and the Gain Limit value
In auto exposure mode, it is set to IRIS priority
Shutter auto
Gain auto
IRIS manual

## Slide 5
Auto Exposure Setting SHUTTER priority.
AE Shutter Speed
Up/Down
- When auto exposure is set to
MANUAL or SHUTTER, the
indicator lights up in red
and the Shutter value changes.
AE B Right
Up/Down
- When auto exposure is set to
Bright, the indicator lights up in
red and the Bright value changes.
In auto exposure mode, it is set to SHUTTER priority.
Shutter speed
Gain auto
IRIS auto